## Slide 1: Guided Transcoding for Next-Generation Video Coding

## Slide 2: Structure of presentation
Introduction to video coding
Adaptive streaming
Guided transcoding
Evaluation environment
Test data

## Slide 3: The need for video coding
Video needs to be compressed to be stored or transmitted
Reduces size several hundreds of times
But encoding takes a long time

## Slide 4: Coding steps
Partitioning
Prediction
Frequency transform
Quantization
Arithmetic coding

## Slide 5: Partitioning
Frames are divided into blocks of different sizes
Encoder tries each option to come up with the most effective partitioning

## Slide 6: Prediction
Data from previous frames are used to predict new frames
The encoder chooses the prediction with the smallest error
The residual is calculated and encoded
This procedure is lossless

## Slide 7: Adaptive streaming
We want to transmit video of different resolutions
Video is divided into small chunks
Depending on the current bandwidth we want to adjust the quality up or down

## Slide 8: Simulcasting
Each resolution is encoded and stored
Requires a lot of space
Many videos may never be used

## Slide 9: Just-in-time transcoding
Lower-resolution videos are generated on-demand
Generally not possible because encoding/transcoding is so expensive

## Slide 10: Guided transcoding
Tries to get around the problems of the two previous methods
Side-information is extracted from the lower-quality videos
The side-info can then be used to quickly regenerate the sequence

## Slide 11: Pruning
Transform coefficients are set to 0
Partitionings and prediction modes are kept (the side-info)
Highest-quality video together with side-info is used to regenerate videos on-demand
Re-encoding step introduces distortion

## Slide 12: Pruned frame

## Slide 13: Partial pruning
Full pruning may still be too slow
If we only prune certain frames then the regeneration becomes faster
Excluding frames that heavily reference other frames will have minimal impact on bit rate but will save complexity

## Slide 14: Partially pruned frame

## Slide 15: Deflation and inflation
All videos encoded from original, so no transcoding loss
Deflation is a two-step process where a prediction is generated and encoded, then subtracted from the transform coefficients of the LQ to create side-info
Inflation reverses process to give a perfect reconstruction

## Slide 16: Evaluation environment
5 standardized H.265 test sequences at 1080p: Kimono, ParkScene, Cactus, BasketballDrive and BQTerrace
Encoded with quantization parameters (QPs): 22, 26, 30, 34
Downscaled to 720p, 540p and 360p
Re-encoded at QP and QP+2
Gives a total of 5×4×3×2 =120 test cases

## Slide 17: Collecting data
We run the simulations on a cluster
Measure bit rate and PSNR (peak signal-to-noise ratio) at several points and store in text files
Script for exporting all data to Excel to calculate averages

## Slide 18: Full pruning
Average bitrates (kbit/s) |  |  |  |  |  |  |  |  | 
 | QP |  |  |  | QP+2 |  |  | Totals | 
 | 1080p | 720p | 540p | 360p | 720p | 540p | 360p | GT gain | Max gain
Kimono1 | 2409 | 1058 | 769 | 477 | 846 | 599 | 363 | 35.5% | 63.0%
ParkScene | 3530 | 1353 | 893 | 472 | 1061 | 682 | 354 | 28.1% | 58.0%
Cactus | 8275 | 2823 | 1944 | 1119 | 2259 | 1527 | 868 | 29.4% | 59.2%
BasketballDrive | 8078 | 2886 | 2048 | 1212 | 2323 | 1615 | 941 | 27.8% | 60.2%
BQTerrace | 13791 | 2626 | 1728 | 887 | 1971 | 1297 | 661 | 25.8% | 48.6%
Averages | 7217 | 2149 | 1476 | 834 | 1692 | 1144 | 638 | 29.3% | 57.8%

## Slide 19: Full pruning
Rate reductions |  |  |  |  |  |  | 
 | QP |  |  | QP+2 |  |  | Totals
 | 720p | 540p | 360p | 720p | 540p | 360p | 
Kimono1 | 58.2% | 56.4% | 55.0% | 57.4% | 55.1% | 52.5% | 55.8%
ParkScene | 48.1% | 49.1% | 51.7% | 47.4% | 47.5% | 48.8% | 48.8%
Cactus | 50.4% | 51.1% | 53.4% | 49.1% | 49.0% | 50.4% | 50.6%
BasketballDrive | 46.8% | 47.2% | 49.4% | 45.7% | 45.3% | 46.2% | 46.8%
BQTerrace | 54.0% | 54.7% | 56.8% | 53.6% | 53.2% | 54.3% | 54.4%
Averages | 51.5% | 51.7% | 53.2% | 50.6% | 50.0% | 50.4% | 51.3%

## Slide 20: Full pruning
Average costs |  |  |  |  |  |  | 
 | QP |  |  | QP+2 |  |  | Totals
 | 720p | 540p | 360p | 720p | 540p | 360p | 
Kimono1 | 17.0% | 9.7% | 4.4% | 11.0% | 6.3% | 2.6% | 8.5%
ParkScene | 15.3% | 8.2% | 3.8% | 9.7% | 5.1% | 2.4% | 7.4%
Cactus | 14.3% | 7.6% | 3.5% | 9.0% | 4.8% | 2.1% | 6.9%
BasketballDrive | 15.8% | 8.8% | 4.1% | 9.9% | 5.5% | 2.5% | 7.8%
BQTerrace | 16.9% | 8.8% | 3.7% | 10.8% | 5.7% | 2.4% | 8.1%
Averages | 15.9% | 8.6% | 3.9% | 10.1% | 5.5% | 2.4% | 7.7%

## Slide 21: Full pruning
Average reconstruction speed (fps) |  |  |  |  |  |  | 
 | 720p |  | 540p |  | 360p |  | Totals
 | QP | QP+2 | QP | QP+2 | QP | QP+2 | 
qp 22/24 | 12.5 | 13.0 | 15.0 | 15.4 | 14.7 | 15.0 | 14.3
qp 26/28 | 16.7 | 17.0 | 20.1 | 20.6 | 19.2 | 19.4 | 18.8
qp 30/32 | 19.8 | 19.9 | 23.9 | 24.3 | 22.2 | 22.2 | 22.1
qp 34/36 | 21.7 | 22.3 | 26.7 | 26.8 | 24.2 | 24.2 | 24.3
Averages | 17.7 | 18.1 | 21.4 | 21.8 | 20.1 | 20.2 | 19.9

## Slide 22: Partial Pruning, level 2
Average bitrates |  |  |  |  |  |  |  |  | 
 | QP |  |  |  | QP+2 |  |  | Totals | 
 | 1080p | 720p | 540p | 360p | 720p | 540p | 360p | GT gain | Max gain
Kimono1 | 2409 | 1058 | 769 | 477 | 846 | 599 | 363 | 28.3% | 63.0%
ParkScene | 3530 | 1353 | 893 | 472 | 1061 | 682 | 354 | 25.2% | 58.0%
Cactus | 8275 | 2823 | 1944 | 1119 | 2259 | 1527 | 868 | 24.3% | 59.2%
BasketballDrive | 8078 | 2886 | 2048 | 1212 | 2323 | 1615 | 941 | 19.4% | 60.2%
BQTerrace | 13791 | 2626 | 1728 | 887 | 1971 | 1297 | 661 | 24.3% | 48.6%
Averages | 7217 | 2149 | 1476 | 834 | 1692 | 1144 | 638 | 24.3% | 57.8%

## Slide 23: Partial Pruning, level 2
Rate reductions |  |  |  |  |  |  | 
 | QP |  |  | QP+2 |  |  | Totals
 | 720p | 540p | 360p | 720p | 540p | 360p | 
Kimono1 | 43.2% | 44.6% | 45.8% | 45.7% | 45.9% | 45.7% | 45.1%
ParkScene | 42.0% | 43.9% | 46.9% | 43.0% | 43.8% | 45.4% | 44.2%
Cactus | 39.9% | 41.5% | 44.2% | 40.8% | 41.3% | 43.1% | 41.8%
BasketballDrive | 29.4% | 32.4% | 36.1% | 31.9% | 33.5% | 35.9% | 33.2%
BQTerrace | 49.2% | 50.0% | 52.5% | 50.8% | 50.4% | 51.8% | 50.8%
Averages | 40.7% | 42.5% | 45.1% | 42.4% | 43.0% | 44.4% | 43.0%

## Slide 24: Partial Pruning, level 2
Average costs |  |  |  |  |  |  | 
 | QP |  |  | QP+2 |  |  | Totals
 | 720p | 540p | 360p | 720p | 540p | 360p | 
Kimono1 | 17.0% | 9.7% | 4.4% | 11.0% | 6.3% | 2.6% | 8.5%
ParkScene | 15.3% | 8.2% | 3.8% | 9.7% | 5.1% | 2.4% | 7.4%
Cactus | 14.3% | 7.6% | 3.5% | 9.0% | 4.8% | 2.1% | 6.9%
BasketballDrive | 15.8% | 8.8% | 4.1% | 9.9% | 5.5% | 2.5% | 7.8%
BQTerrace | 16.9% | 8.8% | 3.7% | 10.8% | 5.7% | 2.4% | 8.1%
Averages | 15.9% | 8.6% | 3.9% | 10.1% | 5.5% | 2.4% | 7.7%

## Slide 25: Partial Pruning, level 2
Average reconstruction speed (fps) |  |  |  |  |  |  | 
 | 720p |  | 540p |  | 360p |  | Totals
 | QP | QP+2 | QP | QP+2 | QP | QP+2 | 
qp 22/24 | 30.4 | 31.5 | 35.9 | 36.7 | 37.4 | 37.8 | 35.0
qp 26/28 | 41.3 | 41.9 | 49.2 | 50.1 | 50.5 | 51.3 | 47.4
qp 30/32 | 48.8 | 52.3 | 60.3 | 62.2 | 61.5 | 61.6 | 57.8
qp 34/36 | 59.1 | 61.8 | 72.1 | 72.2 | 71.6 | 71.7 | 68.1
Averages | 44.9 | 46.9 | 54.4 | 55.3 | 55.2 | 55.6 | 52.1

## Slide 26: Deflation
Average bitrates |  |  |  |  |  |  |  |  | 
 | QP |  |  |  | QP+2 |  |  | Totals | 
 | 1080p | 720p | 540p | 360p | 720p | 540p | 360p | GT gain | Max gain
Kimono1 | 2419 | 1407 | 927 | 536 | 1045 | 690 | 397 | 25.3% | 67.5%
ParkScene | 3552 | 1761 | 1056 | 518 | 1288 | 771 | 380 | 21.4% | 62.4%
Cactus | 8283 | 3557 | 2240 | 1212 | 2662 | 1694 | 920 | 22.2% | 62.8%
BasketballDrive | 8058 | 3647 | 2370 | 1315 | 2738 | 1791 | 997 | 20.8% | 63.8%
BQTerrace | 13605 | 3395 | 2000 | 955 | 2342 | 1439 | 699 | 20.7% | 52.7%
Averages | 7183 | 2753 | 1719 | 907 | 2015 | 1277 | 679 | 22.1% | 61.8%

## Slide 27: Deflation
Rate reductions |  |  |  |  |  |  | 
 | QP |  |  | QP+2 |  |  | Totals
 | 720p | 540p | 360p | 720p | 540p | 360p | 
Kimono1 | 34.9% | 38.5% | 40.1% | 36.7% | 39.2% | 39.6% | 38.2%
ParkScene | 31.5% | 35.8% | 40.8% | 32.5% | 35.8% | 39.6% | 36.0%
Cactus | 32.6% | 37.1% | 41.8% | 33.5% | 36.9% | 40.5% | 37.1%
BasketballDrive | 30.1% | 34.1% | 38.3% | 30.9% | 33.8% | 36.8% | 34.0%
BQTerrace | 36.7% | 41.0% | 46.0% | 38.7% | 41.6% | 45.4% | 41.6%
Averages | 33.2% | 37.3% | 41.4% | 34.5% | 37.5% | 40.4% | 37.4%

## Slide 28: Deflation
Average costs |  |  |  |  |  |  | 
 | QP |  |  | QP+2 |  |  | Totals
 | 720p | 540p | 360p | 720p | 540p | 360p | 
Kimono1 | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
ParkScene | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
Cactus | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
BasketballDrive | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
BQTerrace | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%
Averages | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0% | 0.0%

## Slide 29: Summary
Totals |  |  | 
 | GT gain | Rate reductions | Cost
Full pruning | 29.3% | 51.3% | 7.7%
Partial pruning, lvl 2 | 24.3% | 43.0% | 7.7%
Deflation | 22.1% | 37.4% | 0.0%